## Slide 1: Natural catastrophe risk
Quantification for insurance and reinsurance
Andreas Schraft, Head Catastrophe Perils

## Slide 2: Why insurers and reinsurers need catastrophe models

## Slide 3
loss payment
saves capital
provides capital
Insurer/reinsurer needs to ensure that:
Premium equals expected loss plus margin.
Capital is sufficient to remain solvent after event.
Client
Insurer/Reinsurer
Premium
loss payment
certain
uncertain

## Slide 4: Insured catastrophe losses 1970–2012
Source: Swiss Re, sigma No 2/2013
Billion USD at 2011 values
Earthquake and tsunami
Fire and transportation
Storm and floods

## Slide 5: Growth of values is the main driver of increasing natural catastrophe losses
Increasing values
Concentration of values in exposed areas
Increasing vulnerability
Growing insurance penetration
Changing hazard (climate variability, climate change)
Reasons
Loss history is not a good guide for risk, models are an indispensable tool.
Zurich, around 1900
©Stadt Zürich
Zurich, 2013
©Stadt Zürich

## Slide 6: How we model natural catastrophes

## Slide 7: Four elements to model losses
What is covered? Where? How?
Hazard
Vulnerability
Value distribution
Coverage conditions
Insurance sums
Limits
Excess
Exclusions
etc.
Example
Hurricane “Charley”
Aug 2004
How often? How strong?
How well built and protected?

## Slide 8: Simplest catastrophe model Calculating a loss scenario
Hurricane
Kathrina 2005

## Slide 9: Tropical cyclones in the north Atlantic historical tracks
Historical
~100 years
~1’000 events

## Slide 10: Tropical cyclones in the north Atlantic historical tracks
Historical
~100 years
~1’000 events

## Slide 11: Tropical cyclones in the north Atlantic historical tracks
Historical
~100 years
~1’000 events

## Slide 12: Tropical cyclones in the north Atlantic historical tracks
Historical
~100 years
~1’000 events
Even 100 years worth of historical events are not enough to fully reflect risk.

## Slide 13: Creating additional events based on physical correlation
Hurricane Kathrina with daughter events

## Slide 14: Tropical cyclones in the north Atlantic - historical and probabilistic tracks
historical
~100 years
~1’000 events

## Slide 15: Tropical cyclones in the north Atlantic - historical and probabilistic tracks
historical
~100 years
~1’000 events
probabilistic ~20‘000 years

## Slide 16: Tropical cyclones in the north Atlantic - historical and probabilistic tracks
historical
~100 years
~1’000 events
probabilistic ~20‘000 years
Probabilistic event set aims at reflecting full range of possible storms.

## Slide 17: Hazard footprints
Hazard footprint: Maximum windspeed experienced by each point affected by a storm.
About 200'000 tropical cyclone footprints are prepared in the event / hazard database and used for ratings.
MultiSNAP v11 footprint of Katrina 2005
Notes: 17

## Slide 18: Vulnerability
Wind damage depends on wind speed. Higher wind speeds lead to higher damage. However, loss data from storm events shows huge scatter.
Therefore, buildings need to be classified and described in detail, to be able to describe the behaviour in the model.
Classifications and descriptors we use include
  roof types, e.g. concrete tiles, clay tiles, single ply membrane, wood shingles, metal sheeting
  construction type
  number of storys
  occupancy, e.g. residential, commercial, healthcare

## Slide 19: Four elements to model losses
What is covered? Where? How?
Hazard
Vulnerability
Value distribution
Coverage conditions
Insurance sums
Limits
Excess
Exclusions
etc.
Example
Hurricane “Charley”
Aug 2004
How often? How strong?
How well built and protected?

## Slide 20: Models are not perfect

## Slide 21: Recent earthquakes in Chile, New Zealand and Japan
Chile: Significant losses from industrial facilities, mainly due to business interruption
New Zealand: Back to back, relatively small events on a relatively low hazard zone, generating significant insurance losses, mainly due to liquefaction-related damage
Japan: Major damage and losses from tsunami; complications due to failure of nuclear power plants
 | Chile 27 February 2010 | New Zealand 22 February 2011 | Japan 11 March 2011
Magnitude | 8.8 | 6.3 | 9.0
Energy released (compared to NZ) | 5 600 | 1 | >11 000
Fatalities/missing | 562 | >160 | >20 000
Economic loss, USD bn | 30 | 25 | 210
Insurance loss, USD bn | 8 | 9-12 | 30
Each of the earthquakes surprised us with a larger than anticipated loss.

## Slide 22: Model blind spots revealed by recent earthquakes
Loss Driver | Modelled? | Pass?
Tsunami | Not as such. A few models/markets have a slight loading on the shock rates for coastal locations. | 
Increased seismicity after large event | Not modelled. | 
Liquefaction | Some models/markets consider liquefaction. However, all models by far underestimated impact in Christchurch. | 
Business interruption | Included in most models. However, impact for BI-sensitive industries generally underestimated. | 
Contingent business interruption | Not modelled. Exposure not fully understood. | 
Next surprise? | ? | 

Most vendor models have not yet taken into account experience from recent events.





## Slide 23: Model blind spots revealed by recent earthquakes Most (known) blind spots have been eliminated
Loss Driver | Modelled? | Pass?
Tsunami | Tsunami model for Japan in operation. Global model under development. | 
Increased seismicity after large event | Models are updated within weeks. | 
Liquefaction | Soil quality is part of all new earthquake models. | 
Business interruption | Vulnerabilities in earthquake adjusted globally. | 
Contingent business interruption | Not modelled. Addressed with underwriting measures. | 
Next surprise? | ? | 

Swiss Re is able to quickly learn from events and update models.





## Slide 24: Historical Seismicity and Seismic Sources
Major Historical Events
  1855 M8.0-8.2 on Wairarapa Fault
  2011 M6.1-6.3 in Christchurch
  1931 M7.8-8.0 Hawke's Bay
Major Seismic Sources
  Wellington Fault: ~M7.8 every ~750 years
  Wairarapa Fault: ~M8.0 every ~1000 years
  Alpine Fault: ~M8.0 every ~250 years
Return Period of 2011 EQ (Loss)
  Observed: ~100yrs (considering seismic history)
  Estimated: ~300yrs (considering seismic sources)
Alpine Fault
Wellington and Wairarapa
Faults
Forming an opinion about risk is the starting point for building any model.

## Slide 25: Earthquake New Zealand Variation of earthquake model results
Differing opinions on earthquake risk in New Zealand.
Modelled loss frequency curves for New Zealand market portfolio
Modeled Loss
Return period (years)
0
100
200
300
400
500
600
700
800
900

## Slide 26: Stay in touch
Andreas
Andreas_Schraft@swissre.com
+41 (0)43 285 2757
@ASchraft
Andreas Schraft
openminds.swissre.com

## Slide 27: Legal notice
©2015 Swiss Re. All rights reserved. You are not permitted to create any modifications or derivative works of this presentation or to use it for commercial or other public purposes without the prior written permission of Swiss Re.
The information and opinions contained in the presentation are provided as at the date of the presentation and are subject to change without notice. Although the information used was taken from reliable sources, Swiss Re does not accept any responsibility for the accuracy or comprehensiveness of the details given. All liability for the accuracy and completeness thereof or for any damage or loss resulting from the use of the information contained in this presentation is expressly excluded. Under no circumstances shall Swiss Re or its Group companies be liable for any financial or consequential loss relating to this presentation.