## Slide 1: New “Risk-Targeted” Seismic Maps Introduced into USA Building Codes
Nicolas Luco, Research Structural Engineer
U.S. Geological Survey
Golden, Colorado
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
Notes: * I will treat “risk” and “performance” as synonyms.

## Slide 2: 2012 “International” Building Code
FIGURE 1613.3.1 RISK-TARGETED MAXIMUM CONSIDERED EARTHQUAKE (MCER) GROUND MOTION …
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013

## Slide 3: Development of MCER Maps
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
10
7-10
Notes: * Until recently, the engineering design of new structures to resist earthquakes, and the quantification of seismic risk for existing structures, had been relatively unconnected topics within earthquake engineering.

## Slide 4: http://earthquake.usgs.gov/designmaps/usapp/
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
Notes: 3 groups that I’m a part of

## Slide 5: http://earthquake.usgs.gov/designmaps/usapp/
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
Notes: 3 groups that I’m a part of

## Slide 6: http://earthquake.usgs.gov/designmaps/usapp/
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
Notes: 3 groups that I’m a part of

## Slide 7: Outline of Presentation
Past/present design approaches for seismic safety
Quantification of seismic risk/performance
Recent/future risk-based seismic design approaches
Implications for designing against hazards, in general
Outstanding issues
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013

## Slide 8: Past Seismic Design Approaches
Past and most present design approaches for seismic safety are prescriptive, based on following rules rather than explicitly quantifying performance/risk.
e.g., “If at least seven ground motions [(time series)] are analyzed, the design member forces … are permitted to be taken … as the average of the … values determined from the [building response] analyses …” – ASCE 7 Standard
For earthquake loads/demands, past (and most present) approaches typically design against …
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013

## Slide 9: Deterministic Earthquake Scenarios
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
e.g., USGS “ShakeMaps”
Notes: … and the ground motion intensities predicted to result from them

## Slide 10: Probabilistic Seismic Hazard Maps
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
e.g., ground motion intensity with a uniform
1/2500 annual probability of being exceeded

## Slide 11: Past Seismic Design Approaches
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
Although seismic safety was implied by these past design approaches, …
… the seismic risk for the resulting structures …
(e.g., annual probability of seismically-induced failure)
… was not explicitly quantified in the design process, or in the development of the design process by regulators.

## Slide 12: Seismic Risk Quantification
Meanwhile, for decades now (e.g., ATC 3-06, 1978) …
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
Earthquake
Scientists
Earthquake
Engineers
Seismic
Risk
Probabilistic Seismic
Fragility Curves
Probabilistic Seismic
Hazard Curves
Notes: … earthquake engineers and scientists have worked together to quantify the seismic risk for existing structures.
This is done by coupling probabilistic ground shaking hazard results (at a wide range of hazard levels) from earthquake scientists with probabilistic structural performance assessments from engineers, e.g., …

## Slide 13: Probabilistic Seismic Hazard Curves
Results of Probabilistic Seismic Hazard Analysis (PSHA), pioneered by the late Prof. C. Allin Cornell in 1968.
Notes:
Hazard curves are interpolated to derive aforementioned “hazard maps”.
Shapes of hazard curves can vary significantly with location.
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
Ground Motion Intensity
Annual Prob. of Exceedance
Notes: * For these two locations, the 1/2500-yr ground motions are roughly equal.

## Slide 14: Probabilistic Seismic Fragility Curves
Based on the performance of similar structures in past earthquakes, and/or numerical simulations.
Notes:
Fragility curve depends on the ground motion intensity for which the structure was designed (“Design IM”).
It also depends on the prescriptive requirements that are used to design the structure (e.g., those for buildings vs. nuclear power plants).
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
Notes: * These two example fragility curves are for generic buildings.

## Slide 15: “Risk Integral”
Combination of such hazard and fragility curves is an application of the total probability theorem …
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
Hazard
Risk
Fragility
Notes: The combination of such hazard and fragility curves to quantify risk is often referred to, by earthquake engineers, as the risk integral, which is an application of the total probability theorem.

## Slide 16: “Risk Integral” (Example)
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
Hazard
Risk
Fragility
Ground Motion Intensity, IM=z
P [ Collapse | IM=z ]
P [ IM > z ]
Integrand
Design IM = 1.29g
Design IM = 1.18g

## Slide 17: Risk-Based Design Approaches
Risk-Targeted Maximum Considered Earthquake (MCER) Ground Motions for designing new buildings and other structures, 2012 International Building Code
A Performance-Based Approach to Define the Site-Specific Earthquake Ground Motion, U.S. Nuclear Regulatory Commission (NRC) Regulatory Guide (RG) 1.208, 2007
Development of Next-Generation Performance-Based Seismic Design Procedures for New and Existing Buildings, Applied Technology Council (ATC) Project #58, funded by U.S. Federal Emergency Management Agency (FEMA), 2012
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013

## Slide 18: 2012 International Building Code
FIGURE 1613.3.1 RISK-TARGETED MAXIMUM CONSIDERED EARTHQUAKE (MCER) GROUND MOTION …
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013

## Slide 19: “Risk Integral” (Example)
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
Hazard
Risk
Fragility
Ground Motion Intensity, IM=z
P [ Collapse | IM=z ]
P [ IM > z ]
Integrand
Design IM = 1.29g
Design IM = 1.18g

## Slide 20: Risk-Targeted Ground Motions
2
2
Hazard
Risk
Fragility
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
D
D
Ground Motion Intensity, IM=z
P [ Collapse | IM=z ]
P [ IM > z ]
Integrand
Design IM = 1.50g
Design IM = 0.90g

## Slide 21: Risk-Targeted Ground Motions
Hazard
Risk
Fragility
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
D
D
Ground Motion Intensity, IM=z
P [ Collapse | IM=z ]
P [ IM > z ]
Integrand
Design IM = 1.38g
Design IM = 0.96g

## Slide 22: Risk-Targeted Ground Motions
“Guess” RTGMi
P[Collapse] in 50yrs
= 1%?
Generate fragility curve as a function of RTGMi
Integrate fragility & hazard curves to calculate risk
RTGM Calculated
For a given location …
Yes
No
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013

## Slide 23: Risk-Targeted GM Maps
Note: RTGM maps are coupled with deterministic GM maps to produce the MCER GM maps in the 2012 IBC
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
Notes: Since this calculation of RTGMs is not straightforward, although it is in comparison to PSHA, the site-specific procedures include a second simpler method of calculating RTGMs, …

## Slide 24: Risk Coefficients (CR’s)
Conventional uniform-hazard (2500-yr) GMs interpolated from hazard curves
CR’s =
e.g.,
 | SFBA Location | MMA Location
Risk-Targeted GM | 1.38g | 0.96g
Uniform-Hazard GM | 1.29g | 1.18g
Risk Coefficient (CR) | 1.07 | 0.82
  Risk-Targeted GMs
  Uniform-Hazard GMs
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013

## Slide 25: Risk Coefficient (CR) Maps
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013

## Slide 26: Risk Coefficient (CR) Maps
< 0.85
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013

## Slide 27: Risk Coefficient (CR) Maps
> 1.15
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013

## Slide 28: Preparation of New Design Maps
New MCER GMs
Deterministic GMs
Probabilistic GMs
(Risk-Targeted)
─ In ASCE 7-10
─ In 2009 NEHRP
Risk Coefficients
Uniform-Hazard GMs
X
To relate back
to conventional uniform-hazard (2500-yr) GMs …
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013

## Slide 29
Google “EERI NGA Seminar Presentations” for Video
or email nluco@usgs.gov for just PowerPoint

## Slide 30: Summary
Previous uniform-hazard (2%-in-50yr) probabilistic ground motions …
  Resulted in spatially-variable collapse risk, due to variations in hazard curve shapes
  Considered only a single selected point (2%-in-50yr) on hazard curves
  Were similar in value in Memphis Metro Area and San Francisco Bay Area
New risk-targeted probabilistic ground motions address these issues
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
Notes: Probabilistic hazard curves from which hazard maps are interpolated.

## Slide 31: Summary (continued)
New risk-targeted probabilistic ground motions (RTGMs) …
  Explicitly & uniformly target 1% probability of collapse in a building’s lifetime, ~50 years
  Consider all points on & spatial variations in shapes of hazard curves
  Require a generic fragility that depends on RTGM & effectively considers shapes of hazard curves
  Changes uniform-hazard (2%-in-50yr) ground motions by factor of 0.85-1.15 generally, but as low as 0.70 near New Madrid and Charleston
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
Notes: Probabilistic hazard curves from which hazard maps are interpolated.

## Slide 32: U.S. NRC RG 1.208 (2007)
“Target Risk” = 10-5 annual probability of Onset of Significant Inelastic Deformation (conservative w.r.t. structural failure)
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
Ground Motion Intensity, IM
Annual Prob. of Exceedance
Design IM presented as …
where Design Factor is
and
Notes: Specified tolerable seismic risk level is a …
Design ground shaking intensities presented as …the product of 10-4/year “uniform-hazard” intensities and an approximate design factor given by … where AR is the hazard curve slope (between hazard levels of 10-4 and 10-5/year).
Remove response spectrum

## Slide 33: ATC-58 Project (funded by FEMA)
In addition to building collapse, these new design procedures target annual probabilities of earthquake-induced …
  casualties (Deaths),
  repair costs (Dollars), and
  loss of use (Downtime)
… via generalizations of the risk integral.
Furthermore, risk quantification is “high-resolution,” i.e., …
… fragility curve depends on details of individual elements of the building, not just the design ground motion intensity
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
Notes: Moreover, the resolution of the procedures is such that the fragility curves they quantify depend on details of individual elements of the building of interest (e.g., column dimensions), not just the design ground shaking intensity.
With this approach, the seismic design of buildings will be directly based on risk that is quantified in terms that owners and regulators can relate to.

## Slide 34: Risk-Based Design Approaches
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013
Seismic Risk Quantification
for Existing Structures
Seismic Design
of New Structures
Risk-Based Design
Notes: * Until recently, the engineering design of new structures to resist earthquakes, and the quantification of seismic risk for existing structures, had been relatively unconnected topics within earthquake engineering.

## Slide 35: Implications
Tolerable seismic risk has now been specified quantitatively (vs. qualitative “safe”), which in turn impacts, e.g., …
  evaluation and retrofit of existing structures,
  design for other hazards (e.g., wind, rock falls), and
  prescriptive design procedures (e.g., selection and modification of ground motion time series for structural response simulations).
Risk-based approaches might eventually allay the need for prescriptive design procedures altogether.
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013

## Slide 36: Outstanding Issues
Acceptable/tolerable risk level?
  once in terms of deaths/dollars/downtime, might be borrowed from other hazards?
  for individual structures and aggregation/region?
  must it be geographically uniform?
Validation of risk modeling/quantification (vs. reality)
  hazard and fragility components/curves
  data very scarce at large ground motion intensities
Indian Institute of Science (IISc) Department of Civil Engineering Seminar
“New Risk-Targeted Seismic Maps Introduced into USA Building Codes,” N. Luco, USGS March 6, 2013